 Open Street Maps source

<layer>
id: Name of the layer as in OSM wiki (if type is 0 or 1 the id must be always preceed with it’s name feature. Ex: cable_car is a line so the id must be the concatenation of aerialway with cable_car. This concatenation is done with “_“ (aerialway_cable_car)

layerid: Number used to identify each layer. This number can’t be over 16381. If too layers have the same layerid it will be painted with the first of the two layers. In some cases we can find two or more layers with the same layerid, this happens in some cases like: links, roundabouts, tunnels.

type:
- 0: Line
- 1: Polygon
- 3: Point

visible:
- (-1): Ignores the element(s) when creating the map
- 0: No (elements are created but are not visible on screen)
- 1: Yes

Color: Outbound colour.
- color_r: Red (dec code 0-255).
- color_g: Green (dec code 0-255).
- color_b: Blue (dec code 0-255).

Fill_Color: Fill colour (only for double line).
- fill_color_r: Red (dec code 0-255).
- fill_color_g: Green (dec code 0-255).
- fill_color_b: Blue (dec code 0-255).

near_zoom: defines the zoom to view the information.
- 0: Visible by default.
- 2.000: Visible when map has a 1:2000 scale.
- 5.000: Visible when map has a 1:5000 scale.
- 25.000: Visible when map has a 1:25000 scale.
- 50.000: Visible when map has a 1:50000 scale.
- 100.000: Visible when map has a 1:100000 scale.

far_zoom: defines the zoom to disappear the information

pixel_thickness: width size in pixels.

real_thickness: real width in meters.

name: Internal code or text defined by the user (this name appears on the map data tree)

icon: Simbology

usable_routing: If you can use to navigate.
- 0: Not used.
- 1: Highways.
- 2: Roundabouts.
- 3: Ferry.
- 4: Walking.
- 5: Toll.
- 6: Backroad.

line_type: linetype.
- 0: Solid.
- 1: Dash.
- 2: Dot.
- 3: Dashdot.
- 4: Dashdotdot.
- 5: Null.
- 6: Double.
- 7: Double flat.
- 8: Double Alternate.
- 9: Rail.
- 10: Double Rail.
- 11: Line wall.
- 12: Zig Zag.
- 13: Arrow-32.
- 14: Wheel_arrow-32.
- 15: Arrow_ball-32.
- 16: Wheel_arrow.

transparency: Not used.

max_speed: Maximum speed allowed on the route (this value will be default speed if information is not available when reading map information).

height: Not used.

route_param: Whether or not routable.
- true: Routable.
- false: Non Routable.

parent_layer_id: Numeric code that refers to its origin (point, line, polygon). Only the Main layers are (-1).
- Main Layer Ex: <layer id="POIs" layerid="10300" ... parent_layer_id="-1" ... />
- Item of POIs: <layer id="Fuel" layerid="10301" ... parent_layer_id="10300" ... />
- Main Sub Layer of POIs Ex: <layer id="Restaurant" layerid="10350" ... parent_layer_id="10300" ... />
- Item of Restaurant: <layer id="Chinese" layerid="10351" ... parent_layer_id="10350" ... />

tunnel: If is a tunnel.
- true: Is a tunnel.
- false: Is not a tunnel.

roundabout: If is a roundabout.
- true: Is a roundabout.
- false: Is not a roundabout

ramp: If is an access ramp to highways or trunks.
- true: Is a ramp.
- false: Is not a ramp.

unpaved: If the road is paved or not.
- true: Unpaved.
- false: Paved.